## Slide 1
Types of barcode scanners
Laser, linear and 2D imagers; handheld, cordless, presentation, fixed-mount, wearable scanners and mobile computers - and how to choose.
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/barcode-academy/types-of-barcode-scanners | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
By scan engine - how the scanner reads
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Laser scanner - 1D barcodes - Long reach on 1D codes, familiar red line - Cannot read 2D codes or phone screens; moving parts
• Linear imager (CCD) - 1D barcodes - No moving parts, durable, reads damaged 1D codes and some screens - No 2D codes; shorter range than laser
• 2D area imager - 1D and 2D (QR, Data Matrix, PDF417) and screens - Omnidirectional - no need to align the code; reads phone screens and UPI QR codes...
• Long-range / extended-range imager - 1D and 2D from metres away - Reads pallet and rack labels from the ground or a forklift - Higher cost; for...
• DPM imager - Direct part marks - Reads dot-peen and laser-etched codes on metal and plastic parts - Specialised for manufacturing and automotive
MINDWARE

## Slide 3
By form factor - how the scanner is used
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Handheld corded scanners - the everyday scanner for billing counters and desks, connected by USB.
• Handheld cordless (Bluetooth / radio) scanners - move freely around a shop or store room; the base charges the battery.
• Rugged / industrial handhelds - survive drops, dust and water in warehouses and factories.
• Presentation (hands-free) scanners - sit on the counter; the customer or cashier simply shows the item or phone.
• In-counter and bioptic scanners - built into supermarket checkouts, reading from several angles at once, often with a weighing scale.
• Fixed-mount scanners - mounted over conveyors and production lines to scan automatically, connected to PLCs and software.
• Wearable and ring scanners - worn on the hand or wrist so warehouse pickers keep both hands free.
MINDWARE

## Slide 4
By form factor - how the scanner is used (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Mobile computers (PDAs) - Android devices with a built-in scanner, screen and Wi-Fi/4G, running inventory, picking and delivery apps.
• Pocket / companion scanners - small Bluetooth scanners paired with a phone or tablet for field sales and stock checks.
• Smartphone camera apps - fine for occasional scans; much slower than a dedicated scanner for volume work.
MINDWARE

## Slide 5
How scanners connect
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Most scanners act like a keyboard (USB HID): the scanned data appears wherever the cursor is, so they work with any billing or ERP software without drivers. Others use virtual COM/serial ports, Bluetooth, or Ethernet and industrial protocols for fixed-mount...
MINDWARE

## Slide 6
How to choose a barcode scanner
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Which codes? Only 1D on your own labels - a linear imager is enough. QR, Data Matrix, GS1 Digital Link, UPI or phone screens - choose a 2D imager.
• Where? Shop counter, warehouse, cold store, factory floor or outdoors - decides rugged rating, cordless range and battery.
• How many scans a day? High volume calls for presentation, in-counter or fixed-mount scanners.
• Distance and label size? Tiny jewellery or electronics labels need high-density scanners; rack labels need long-range imagers.
• Connection? USB, Bluetooth, mobile computer or integration with a conveyor system.
• Mindware supplies and services scanners and mobile computers from brands such as Datalogic , Seuic and Zebra - see all barcode scanners and mobile computers . Scanners are covered hands-on in Weeks 7-8 of the Barcode Technology Course .
MINDWARE

## Slide 7
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE