## Slide 1
What is a barcode?
How a barcode stores data, how scanners read it and the parts of a barcode.
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/barcode-academy/what-is-a-barcode | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why barcodes matter
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Typing a 13-digit product number by hand is slow, and people make mistakes. A barcode scanner reads the same number in a fraction of a second, with far fewer errors.
MINDWARE

## Slide 3
What a barcode actually contains
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Most retail barcodes do not contain the product name or price. They contain an identification number - for example a GTIN (Global Trade Item Number).
• Other barcodes carry more: a GS1-128 barcode on a carton can hold the product number, batch, expiry date and quantity; a QR code can hold a full web address, a vCard or a payment string.
MINDWARE

## Slide 4
Parts of a barcode
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Bars and spaces (or modules) - the pattern that encodes the data.
• Quiet zones - blank margins on both sides. If text or a box edge crowds them, scanners struggle.
• Start and stop patterns - tell the scanner where the code begins and ends, and in which direction it is being read.
• Check digit - a final digit calculated from the others, so the scanner can detect a bad read.
• Human-readable text - the digits printed under the bars, so a person can type them if the code is damaged.
• X-dimension - the width of the narrowest bar. It decides how big the barcode must be and which printer resolution you need.
MINDWARE

## Slide 5
How a scanner reads a barcode
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A scanner lights up the code and measures the light reflected back. Dark bars absorb light; light spaces reflect it.
• The decoder turns the pattern into characters and sends them to the computer, usually as if they had been typed on a keyboard.
MINDWARE

## Slide 6
1D and 2D barcodes
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• 1D (linear) barcodes such as EAN-13 and Code 128 store data in the widths of vertical bars - typically up to a few dozen characters. 2D barcodes such as QR codes and Data Matrix store data in a grid of squares, so they hold far more (hundreds to a few...
MINDWARE

## Slide 7
What you need to use barcodes
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Numbers - for retail products, GS1 barcode numbers ( barcode registration ); for internal use, your own numbering.
• Labels - the right label material and size for the surface and environment.
• Printer and ribbon - a thermal barcode printer and, for thermal transfer labels, the matching ribbon.
• Software - label design software such as BarTender, or printing from your billing or ERP system.
• Scanners - handheld, fixed or mobile computers, connected to your software.
• Mindware supplies all five - and makes the labels in-house in New Delhi.
MINDWARE

## Slide 8
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE