## Slide 1
RFID for Car Parking: Step-by-Step Implementation
An RFID car parking system lets registered vehicles enter and exit without stopping, while visitors are handled with tickets, QR codes or OTPs. This chapter walks through every phase, from surveying the lanes and choosing...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/car-parking-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why RFID for car parking
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Most parking problems at housing societies, office campuses, malls and hospitals are about people, not cars: a guard writing numbers in a register, a queue at the gate during the morning rush, residents complaining that visitors take their slots, and no...
• RFID does not replace the guard; it frees the guard to deal with the exceptions - visitors, deliveries, emergencies - while regular users flow through. It also produces clean data: entry and exit logs, slot occupancy and pass validity, which a manual register...
• Who uses which method
• Residents / owners - Dedicated UHF windshield tag - One tag per vehicle, linked to flat number and vehicle registration
• Staff / employees - Windshield tag, sometimes plus employee card - Linked to HR status so leavers are blocked automatically
• Monthly pass holders (malls, hospitals) - Windshield tag with validity dates - Pass expires in software; no need to collect the tag
• Visitors - QR code, OTP or printed ticket - Pre-registered by a host or issued at the gate
MINDWARE

## Slide 3
Why RFID for car parking (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Delivery and service vehicles - Ticket or temporary pass, often with ANPR - Time-limited, restricted to certain zones
MINDWARE

## Slide 4
Building blocks of an RFID parking lane
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Windshield tags
• The standard credential is a passive UHF (EPC Gen2 / ISO/IEC 18000-63) windshield label stuck on the inside of the front glass, usually near the top centre or behind the rear-view mirror. Good parking tags are tuned for glass, use a tamper-evident...
• Dedicated parking tag vs reading an existing FASTag
• Every car in India now carries a FASTag, which is itself a UHF RFID tag (see FASTag and RFID in India ). Some parking systems can read the FASTag's ID and use it as the vehicle credential, which avoids issuing a second tag.
• Readers and antennas
• Each lane needs a long-range UHF reader with an antenna aimed at the approach zone. Integrated reader-antenna units mounted on a pole or gantry are common for parking because they are simple to install; separate readers with external antennas give more...
• Boom barrier and controller
MINDWARE

## Slide 5
Building blocks of an RFID parking lane (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The reader (or a small access controller between reader and software) drives the barrier through a dry-contact relay or GPIO output: a short pulse means "open". The barrier controller handles the motor, the arm timing and safety.
• Loop detectors and sensors
• An inductive loop cut into the road (or a radar / photo-eye sensor) detects the presence of a vehicle. Typically one loop before the barrier arms the reader or confirms that a vehicle is actually there, and one loop under or after the arm keeps it open while...
• ANPR cameras as a complement
• Automatic number plate recognition cameras read the registration plate. They are useful for visitors, for evidence (a photo for every entry), and as a cross-check that the tag belongs to the car carrying it.
• Tip: Ask for a reader that supports a local allow-list or offline mode. If the network or server goes down, the lane should still open for registered tags and sync the logs later, instead of creating a queue at the gate.
MINDWARE

## Slide 6
Designing the visitor flow
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Visitors are where most parking projects become complicated, so design this flow early rather than after the RFID lanes are live.
• Pre-registered visitors: a resident or host creates a visit in an app or web portal; the visitor receives a QR code or OTP by SMS or messaging app...
• Walk-in visitors: the guard enters the vehicle number and destination on a tablet, or a ticket dispenser issues a barcode or QR ticket; payment, if...
• Separate or shared lanes: where traffic allows, keep a dedicated RFID lane for residents and a manned lane for visitors. At small gates a single lane...
• Whatever you choose, every visitor entry should create a record in the same software as RFID entries, so that occupancy and audit reports include everyone.
MINDWARE

## Slide 7
Parking software: what it must do
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Vehicle database: tag ID, vehicle registration, owner, flat or department, vehicle type, photo if available.
• Allow / deny lists: active, suspended, expired and blacklisted tags; time-based rules (for example staff allowed only on working days).
• Event logs: every entry, exit, manual opening and denied attempt with timestamp, lane and operator.
• Slot counting and zones: count of vehicles in each zone, "full" status, and optionally assigned slots per resident.
• Display boards: "spaces available" signs at entry and floor level, driven from the count.
• Passes and payments: monthly passes with validity dates, renewals, visitor tariffs and integration with a payment gateway or cash counter.
• Anti-passback: a tag that has entered cannot enter again until it has exited, which stops one tag being passed back to a second car.
MINDWARE

## Slide 8
Parking software: what it must do (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Reports and alerts: peak-hour traffic, overstays, repeated read failures per lane, tags not seen for months.
• Watch out: A parking database holds personal data - names, flat numbers, phone numbers and movement history. Under India's DPDP Act 2023, collect only what you need, tell users how it is used, restrict who can see logs and set a retention period.
MINDWARE

## Slide 9
Step-by-step implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Survey the lanes. Measure lane widths, approach distance, speed, gradient and turning space. Note where poles or gantries can go, power and network...
• Choose and test tags. Collect a sample of vehicles that represent your users - hatchbacks, SUVs, premium cars with coated glass, two-wheelers if...
• Register vehicles and issue tags. Collect registration certificates or vehicle details, link each tag ID to the vehicle record, and fix the tag in...
• Install readers and barriers. Mount readers and antennas, cut loops, run power and network, wire the relay or GPIO output to the barrier controller...
• Configure the software. Import the vehicle database, set rules, link lanes to zones, connect display boards and set up user roles for guards...
• Pilot one lane. Run one entry and one exit lane for two to four weeks with a guard present. Measure read rate, average opening time, false openings...
• Go live. Extend to all lanes, communicate the rules to residents or staff, and keep a guard on duty at peak hours for the first weeks.
MINDWARE

## Slide 10
Step-by-step implementation (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Maintain. Review exception reports weekly, clean and check loops and barriers monthly, replace damaged tags, deactivate tags of sold vehicles, and...
• Illustrative timeline
• The timeline below is illustrative for a mid-sized site with two to four lanes; your project may be faster or slower depending on civil work, approvals and number of vehicles.
• Lane survey and requirement sign-off - 1 week - Lane drawings, traffic data, user groups
• Tag and reader testing - 1 week - Chosen tag type and mounting positions
• Vehicle registration and tagging camps - 1-3 weeks - Tagged vehicles linked to database
• Installation (readers, loops, barriers, cabling) - 1-2 weeks - Working lanes
MINDWARE

## Slide 11
Equipment checklist
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Long-range UHF reader (integrated or with external antenna) - Lane - Reads windshield tags in the approach zone
• Pole, gantry or wall mount - Lane - Holds the reader at the tested height and angle
• Windshield tags, plus some headlamp / number-plate tags - Vehicle - Vehicle credential
• Boom barrier with controller - Lane - Physical control, opened by relay / GPIO
• Loop detectors or presence sensors - Lane (usually two) - Vehicle detection, safety, anti-tailgating
• Access controller or edge PC (if not built into reader) - Gate - Local decisions, offline allow-list
• Ready-made RFID lane and gate products are listed under RFID gate systems .
MINDWARE

## Slide 12
Troubleshooting common problems
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tag not read on some cars
• Many modern cars have metallised, heat-reflective or heated windshields, which block or weaken UHF signals. Some have a small uncoated area (often near the mirror) where a tag works; check the vehicle manual or test spots.
• Angle and position
• A tag stuck low on the glass, at the far edge, or behind a dark tint band may sit outside the antenna beam. Standardise the tag position for each vehicle class and re-aim antennas so the beam covers where tags actually are, not where the drawing assumed.
• Speed
• If drivers approach fast, the tag may be in the read zone for too short a time, or the barrier may not open in time. Use speed breakers before the lane, increase the read zone slightly upstream, and set the reader to report a tag as soon as it is first seen.
• Tailgating and cross-reads
MINDWARE

## Slide 13
Troubleshooting common problems (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tailgating is controlled by loops: the arm closes after each vehicle clears the exit loop, and the next opening needs a new valid read. Anti-passback stops tag sharing.
• Example: A residential society pilots one entry lane and finds that about one car in twenty is not read. On inspection, almost all are premium models with coated windshields.
MINDWARE

## Slide 14
KPIs and common pitfalls
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• KPIs to track
• First-attempt read rate per lane - registered vehicles opened without guard help.
• Average entry time from arrival to barrier open, especially at peak hours.
• Manual openings per day and the reasons logged for them.
• Unauthorised entries - tailgating events and denied tags.
• Occupancy accuracy - software count vs a physical count at a fixed time.
• Uptime of readers, barriers and software.
MINDWARE

## Slide 15
KPIs and common pitfalls (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Pitfalls
• Handing out tags for users to stick themselves - positions vary and read rates drop.
• Skipping loops or sensors to save cost, then facing tailgating and safety issues.
• No visitor process, so guards fall back to the paper register and data is incomplete.
• No offline mode, so a server or internet outage stops the gate.
• Never deactivating tags of sold vehicles or departed staff.
• Choosing the cheapest tag without testing it on coated windshields.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE