## Slide 1
EPC Encoding & Tag Memory
A UHF RFID tag stores its data in four memory banks, and the EPC bank usually holds a GS1 identifier packed into binary. This chapter explains each bank, walks through converting a real GTIN and serial number into an SGTIN-96 hex...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/epc-encoding-memory | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why encoding matters
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A passive UHF tag is, at heart, a small memory chip connected to an antenna. Whatever you write into that memory is all the reader will ever get back.
• This chapter focuses on EPC Gen2 (ISO/IEC 18000-63) tags, the standard for UHF described in RFID Standards & Regulations . HF and NFC tags organise memory differently (blocks and sectors, or NDEF files), but many of the same principles apply.
MINDWARE

## Slide 3
The four Gen2 memory banks
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Every Gen2 chip divides its memory into four logically separate banks, numbered 0 to 3. Readers address them by bank number and word offset, where one word is 16 bits.
• 00 - Reserved - Kill password (32 bits) and access password (32 bits) - 64 bits
• 01 - EPC - CRC-16, Protocol Control (PC) word, the EPC itself, optional extended PC (XPC) words - EPC of 96 bits is most common; many chips allow...
• 10 - TID - Tag identifier: chip manufacturer, model and, on most modern chips, a unique serial - Commonly 64-96 bits; written and locked at the...
• 11 - User - Optional free memory for application data - None on many chips; up to several kilobits on others
• Bank 00 - Reserved
• Holds two 32-bit passwords. The kill password must be non-zero for the kill command to work.
MINDWARE

## Slide 4
The four Gen2 memory banks (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Bank 01 - EPC
• The first word (offset 00h) is a CRC-16 that the tag computes itself; you never write it. The second word (offset 10h, counted in bits) is the Protocol Control (PC) word .
• Bank 10 - TID
• The TID begins with a class identifier ( E2 for chips registered under the GS1 EPCglobal scheme), followed by a manufacturer designer ID and a tag model number. Most modern UHF chips also carry a factory-programmed unique serial number in an extended TID.
• Bank 11 - User
• Optional memory for extra data such as maintenance dates, batch details or a small record. It is slower to read than the EPC (it needs a separate Read command after inventory), so keep it for data you truly need on the tag.
MINDWARE

## Slide 5
SGTIN-96 structure
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The GS1 EPC Tag Data Standard defines the SGTIN (Serialised Global Trade Item Number). A normal barcode GTIN identifies a product type - every bottle of the same shampoo shares one GTIN.
• Header - 8 - Identifies the scheme. SGTIN-96 is 00110000 = 30 hex.
• Filter - 3 - Packaging level, so readers can select quickly. 1 = point-of-sale trade item, 2 = full case for transport, 6 = unit load, 0 = all others.
• Partition - 3 - How the next 44 bits are split between company prefix and item reference.
• GS1 Company Prefix - 20-40 - Your company number, issued by GS1 (in India, by GS1 India).
• Item reference - 24-4 - Indicator digit followed by the item reference digits of the GTIN.
• Serial number - 38 - A numeric serial from 0 to 274,877,906,943.
MINDWARE

## Slide 6
SGTIN-96 structure (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The partition table
• A GTIN contains 13 digits of company prefix plus item reference (the check digit is dropped). Company prefixes vary in length from 6 to 12 digits, so the partition value records the split:
• 0 - 40 / 12 - 4 / 1
• 1 - 37 / 11 - 7 / 2
• 2 - 34 / 10 - 10 / 3
• 3 - 30 / 9 - 14 / 4
• 4 - 27 / 8 - 17 / 5
MINDWARE

## Slide 7
Worked example: GTIN + serial to SGTIN-96 hex
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Let us encode one item from start to finish. The numbers are illustrative: assume a company whose GS1 Company Prefix is 8901234 (7 digits; 890 is the GS1 India prefix range).
• Step 1 - Check the GTIN and make it 14 digits
• Verify the check digit. Take the first 12 digits, 8 9 0 1 2 3 4 5 6 7 8 9, and multiply alternately by 1 and 3 from the left: 8 + 27 + 0 + 3 + 2 + 9 + 4 + 15 + 6 + 21 + 8 + 27 = 130.
MINDWARE

## Slide 8
Worked example: GTIN + serial to SGTIN-96 hex (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Check digit: 0 - dropped, because it can be recalculated
• The SGTIN item reference is the indicator digit followed by the item digits: 056789 , 6 digits. A 7-digit company prefix means partition 5 (24 bits for the prefix, 20 bits for the item reference).
• Step 3 - Convert each field to binary
• Header - 48 (30 hex) - 8 - 00110000
• Filter - 1 - 3 - 001
• Partition - 5 - 3 - 101
• Company prefix - 8901234 (87D272 hex) - 24 - 100001111101001001110010
MINDWARE

## Slide 9
Other EPC schemes: SSCC, GRAI, GIAI and more
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The same header-filter-partition pattern is used for other GS1 keys. The most common 96-bit schemes are:
• SGTIN-96 - 30 - Individual trade item (GTIN + serial) - Retail apparel, FMCG, pharma units
• SSCC-96 - 31 - Logistics unit (company prefix + serial reference) - Pallets, shipping cartons
• SGLN-96 - 32 - Physical location (GLN + extension) - Dock doors, shelves, zones
• GRAI-96 - 33 - Returnable asset (asset type + serial) - Crates, kegs, gas cylinders, roll cages
• GIAI-96 - 34 - Individual asset (company prefix + asset reference) - IT equipment, tools, furniture, fixed assets
• Where a numeric 38-bit serial is not enough, for example when serials contain letters, the SGTIN-198 scheme (header 36 ) supports alphanumeric serials of up to 20 characters, at the cost of a longer EPC bank. Newer editions of the Tag Data Standard also add...
MINDWARE

## Slide 10
Other EPC schemes: SSCC, GRAI, GIAI and more (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Example: A manufacturer of returnable plastic crates assigns each crate type an asset type number and gives every crate a serial, encoded as GRAI-96. When crates return from distributors, a gate reader counts them by type automatically, and the software flags...
MINDWARE

## Slide 11
Lock, permalock and kill
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Lock states
• The Gen2 Lock command sets protection independently for each password and for the EPC, TID and User banks. Each can be:
• Unlocked - writable in the open or secured state.
• Locked - writable only in the secured state, that is after the reader presents the correct access password. For the passwords, lock also blocks...
• Permalocked - permanently locked; can never be changed again.
• Permaunlocked - permanently writable; can never be locked.
• Lock protects against writing, not against reading: the EPC and TID banks remain readable by any Gen2 reader. Hiding data from readers needs Gen2v2 Untraceable or other chip-specific privacy features.
MINDWARE

## Slide 12
Lock, permalock and kill (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Kill
• The kill command permanently disables a tag. It only works if the kill password is non-zero and the reader supplies it correctly.
• Watch out: If you lock the EPC bank with an access password, record that password securely. Losing it means the tag can never be re-encoded.
MINDWARE

## Slide 13
TID-based anti-cloning
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Copying an EPC is trivial: anyone with a writable blank tag can encode the same 24 hex characters. The TID, however, is written by the chip manufacturer and permalocked, and on serialised chips it is unique.
• At encoding time, read the TID and store the EPC-TID pair in your database.
• Whenever a tag is read in a sensitive process (returns, authentication, high-value check-in), read both EPC and TID.
• If the EPC exists but the TID does not match, flag a likely clone or relabelled item.
• This defeats casual cloning with ordinary blank tags. It does not stop a determined attacker using specialist equipment that can emulate a tag's TID.
MINDWARE

## Slide 14
Encoding best practices
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Use GS1 identifiers with your own company prefix for anything that leaves your premises. Home-made numbers risk collisions with other companies' tags...
• Guarantee unique serials. Allocate serials centrally, never from two printers that might overlap. Duplicate EPCs break inventory counts.
• Set the filter value correctly so readers can select only items, only cases or only pallets.
• Encode, then verify. Read back every tag after writing and reject or void failures. Good RFID printers do this automatically and overstrike bad...
• Capture the TID with every encoded EPC.
• Lock the EPC with a non-default access password where tampering is a risk; permalock only when the data must never change.
• Keep personal data off the tag. Store a reference number on the tag and keep names or health data in a secured database.
MINDWARE

## Slide 15
Encoding best practices (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Print the human-readable and barcode form of the same identifier on the label as a fallback.
• The practical side of high-volume encoding - printer calibration, inlay position and void handling - is covered in RFID Printing & Encoding , and suitable labels are on our UHF RFID labels page.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE