## Slide 1
RFID for Exporters: Step-by-Step Guide
Many overseas retailers and brands now ask their suppliers to deliver goods already carrying RFID tags. This chapter walks an Indian exporter through the whole job, from decoding the buyer tagging specification and getting GS1...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/exporters-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why overseas buyers ask for RFID
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• If you export garments and knitwear from Tiruppur, Noida or Bengaluru, leather goods and footwear, home textiles, pharmaceuticals, auto parts or electronics, there is a growing chance that a buyer has asked you to deliver goods with RFID tags already applied....
• The reasons are practical. A distribution centre can read every item in a sealed carton in seconds instead of opening it and scanning barcodes one by one.
• Many large retailers ask suppliers to source-tag specific departments first, often apparel, footwear and home goods, and extend the programme over time. The details differ from buyer to buyer, so the golden rule of this chapter is simple: always follow the...
MINDWARE

## Slide 3
Step 1: Read and decode the buyer tagging specification
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The tagging specification (sometimes called a source tagging guide or vendor RFID manual) is usually a PDF of 20 to 80 pages. Read it end to end and convert it into a one-page internal summary.
• Scope: which departments, product categories and ship dates the programme covers.
• Approved inlays and chips: a list of inlay models (antenna plus chip) the buyer accepts. Many programmes rely on independent test labs and...
• Tag format and placement: whether the tag sits in a hang tag, price ticket, sewn-in care label or adhesive label, and exactly where on the product it...
• Encoding: the EPC scheme, usually SGTIN-96 based on GS1 GTINs, plus rules for the filter value, serial numbers and whether user memory or passwords...
• Label artwork: the visible print, often including a logo that tells consumers the label contains RFID, and barcode and text positions.
• Carton and pallet labelling: shipping labels, often with an SSCC barcode, and whether cartons also need an RFID tag.
MINDWARE

## Slide 4
Step 1: Read and decode the buyer tagging specification (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Data exchange: whether the advance ship notice (ASN) must list EPCs, or only GTIN quantities per carton.
• Testing and certification: any sample approval, first-shipment audit or ongoing quality checks, and the penalties for non-compliance.
• Tip: Keep a version log of the specification. Buyers update their guides, and a change in an approved inlay or label template can quietly turn a compliant shipment into a non-compliant one.
MINDWARE

## Slide 5
Step 2: Get your GS1 identifiers in order
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A standard retail RFID tag carries an Electronic Product Code (EPC). The most common scheme, SGTIN-96, combines a GS1 company prefix, an item reference (together these come from the product GTIN) and a serial number that makes each individual item unique.
• Whichever applies, build a clean GTIN master : one row per style, colour and size (or per SKU for non-apparel), with the GTIN, description and buyer item number. Most encoding errors trace back to a wrong GTIN in this table, so lock it down and control...
MINDWARE

## Slide 6
Step 3: Choose a label converter or in-house encoding
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• You have two broad options for producing encoded tags.
• Option A: Label or tag converter service
• A converter is a company that turns approved inlays into finished hang tags, tickets or labels, prints the artwork and variable data, encodes the EPC and verifies every tag. You send an order file (GTINs and quantities per purchase order), and receive tags in...
• Option B: In-house encoding with RFID printers
• You buy pre-converted blank RFID labels or tickets from an approved source, then print and encode them on your own RFID printers, driven by your software. This gives control over lead times and suits factories with high volumes, many small orders or frequent...
• Start-up effort - Low - Medium to high (printers, software, training)
• Lead time for tags - Depends on converter, typically days - Same day once set up
MINDWARE

## Slide 7
Step 3: Choose a label converter or in-house encoding (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Serial number management - Converter manages - You manage
• Artwork compliance - Converter usually holds approved templates - You must match templates exactly
• Best for - New suppliers, moderate volumes - High volume, fast fashion, many small orders
MINDWARE

## Slide 8
Step 4: Set up encoding data and serialization
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Every tag must carry a unique EPC. In SGTIN-96 the GTIN part repeats for every item of the same SKU, so uniqueness comes from the serial number.
• Keep one serial counter per GTIN (or follow the serial range rules in the buyer spec, if it allocates ranges to suppliers or converters).
• Never reuse a serial, even for reprints. A reprinted tag gets a new serial and the old one is marked void.
• If you use more than one converter or encoding location for the same GTINs, split the serial ranges so they can never overlap.
• Store every encoded EPC with the purchase order, carton and date. This record is what you use to build EPC-level packing lists and to answer buyer...
• Use the filter value the specification asks for; for item-level retail tags this is usually the value for a point-of-sale item.
• Watch out: Duplicate EPCs are one of the most damaging errors. Two items with the same EPC look like one item to the buyer's system, so stock counts are wrong from the first day.
MINDWARE

## Slide 9
Step 5: Apply tags at the right production stage
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Where you attach the tag depends on its format. Sewn-in care labels with an RFID inlay must be added on the sewing line, so the encoded labels must reach the line sorted by size before the bundle starts.
• Follow the placement drawing exactly. The buyer has tested that position for readability in folded, hung and boxed states.
MINDWARE

## Slide 10
Step 6: Verify every carton at packing
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Verification is where compliant suppliers separate themselves from the rest. Before a carton is sealed, read it with an RFID tunnel (a shielded conveyor tunnel with fixed reader antennas) or a carton reading station, or with a handheld reader for low volumes.
• Count matches the expected quantity per GTIN: carton passes.
• Fewer tags than expected: find the item with a dead or missing tag, replace the tag and re-read.
• More tags than expected or a wrong GTIN: wrong item packed or stray tags nearby; correct and re-read.
• Duplicate or unknown EPCs: stop and investigate the encoding source.
• Shield the verification area so the reader does not pick up tags from neighbouring cartons or rolls of spare tags. Keep the read results; they become your proof of what was shipped.
• Example: A knitwear exporter packing 24 pieces per carton runs each sealed-but-open carton through a tunnel. The screen shows 23 reads.
MINDWARE

## Slide 11
Step 7: Build the EPC-level packing list, ASN and dispatch
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Once all cartons pass, generate the packing list. Depending on the specification, the ASN may list only GTIN quantities per carton or every EPC per carton, linked to the carton SSCC.
MINDWARE

## Slide 12
Market notes: EU, US, UK, Middle East and Russia/EAEU
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Requirements come mainly from individual buyers, not from a single law, so expect differences between customers in the same country. Tags must work in both India (865-867 MHz) and the destination: approved retail inlays are generally designed for global UHF...
• US and UK: mature retail source-tagging programmes in apparel, footwear and general merchandise; strict artwork and verification rules.
• EU: widespread use in fashion and sports retail; also watch for upcoming product traceability and digital product passport rules, which may influence...
• Middle East: large regional retail groups and franchise operators use RFID for store inventory; specifications often follow the brand owner's global...
• Russia and EAEU: Russia's mandatory marking system, Chestny ZNAK, mainly uses DataMatrix codes, but some categories, such as fur products, have used...
MINDWARE

## Slide 13
Exporter RFID checklist
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Latest tagging specification received and summarised - Merchandiser / compliance - One-page summary signed off
• GTIN source confirmed (buyer or own GS1 prefix) - Merchandiser - GTIN master locked
• Approved inlay and tag format confirmed - Purchase - Converter or label supplier confirms model
• Artwork approved - Compliance - Buyer approval on file
• Serialization rules and ranges set - IT / converter - No overlap between sources
• Tag placement trained on lines - Production - Placement drawing at every station
MINDWARE

## Slide 14
Illustrative rollout timeline
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The timeline below is illustrative only; real durations depend on the buyer, your volumes and whether you use a converter.
• 1-2 - Study specification, confirm GTIN source, shortlist converter or printer setup
• 2-4 - Artwork approval, approved inlay ordered, serialization and data flow designed
• 4-6 - Verification station installed, staff trained, internal trial on one style
• 6-8 - Buyer samples or pilot shipment, fix issues, test ASN
• 8 onwards - Full production; monthly review of KPIs and specification updates
MINDWARE

## Slide 15
KPIs and common pitfalls
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• KPIs to track
• Encoding yield: share of tags encoded and verified first time.
• Carton first-pass rate: cartons that pass verification on the first read.
• Duplicate EPC count: target zero.
• Buyer compliance score and chargeback value per season.
• Tag lead time: days from order to tags on the line.
• Pitfalls
MINDWARE

## Slide 16
KPIs and common pitfalls (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Using an inlay that is not on the approved list because it was cheaper or available sooner.
• Dead tags from crushing, heat presses, sharp tagging guns or static damage.
• Wrong placement, especially near metal accessories that detune the tag.
• Duplicate EPCs from uncontrolled serial counters.
• Wrong GTIN for a size or colour, so the buyer receives the right count of the wrong item.
• Stray tags read during verification, hiding a real shortage.
• Ignoring specification updates between seasons.
MINDWARE

## Slide 17
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE