## Slide 1
RFID for Inventory Management: Step-by-Step Implementation
RFID turns stock counting from a slow, item-by-item job into a quick sweep with a handheld reader, and fixed readers can keep counts updated continuously. This chapter shows how to plan and roll out RFID inventory management in...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/inventory-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
What RFID changes in inventory
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• With barcodes, every item has to be found, turned so its label faces the scanner, and scanned one at a time. That is why full stock counts happen once or twice a year and why the system quantity and the shelf quantity drift apart in between.
• The same approach works across very different inventories: apparel and footwear in retail stores, stockrooms and back-of-store areas, spare parts in maintenance stores, IT assets such as laptops and monitors, and medical consumables and equipment in...
MINDWARE

## Slide 3
Phase 1: Define what is counted
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Before talking about tags, write down exactly what you want to know and at what level:
• Item level - every unit has its own tag and unique serial. Best for apparel, footwear, electronics, IT assets, instruments and high-value spares....
• Case or carton level - one tag per carton, bin or tote, with the contents known from the packing list. Suitable for low-value, fast-moving...
• Asset level - fixed and movable assets that are counted for audit and location rather than sold.
• Also decide where stock lives (sales floor, stockroom, store, ward, warehouse location), how often you need a count, and which decisions the data will drive - replenishment, audit, shrink investigation, expiry control. Projects that skip this step tend to tag...
• Tip: Start with a single category where count errors clearly cost money - for example size-and-colour apparel, high-value spares or IT assets - rather than the whole inventory. Success there pays for the next phase.
MINDWARE

## Slide 4
Phase 2: Choose tags and decide who tags
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tag choice
• Tag selection depends on the material being tagged, the read distance needed, memory requirements and cost. Paper or fabric hang tags and labels suit apparel; on-metal tags suit tools, laptops and metal parts; liquid-tolerant designs suit bottles and medical...
• Source tagging vs in-house tagging
• Source tagging means the manufacturer or supplier applies and encodes the tag before the goods reach you. It is the cheapest and most consistent option at scale, but it needs supplier agreements, a common encoding standard (usually GS1 SGTIN for retail goods)...
• In-house tagging means you print, encode and apply tags yourself - at receiving, in a tagging room, or for existing stock during the initial rollout. You will need RFID printers for labels and encoders for pre-made tags; see RFID printers and RFID encoders...
• Watch out: Duplicate EPCs are one of the hardest problems to clean up later. Make sure every encoding station draws serial numbers from one controlled source and that the software rejects duplicates at the moment of encoding.
MINDWARE

## Slide 5
Phase 3: Plan how you will read
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Handheld cycle counts
• For most sites the first and most valuable step is periodic counting with a handheld reader - a sled attached to a smartphone or an all-in-one device. The operator walks a defined route, sweeping shelves and racks, and the app compares what it found with what...
• Fixed and overhead reading
• Where you need near real-time visibility - stock moving between stockroom and sales floor, items leaving a store, assets leaving a ward - fixed readers at doorways or ceiling-mounted readers covering an area keep the picture updated without anyone counting....
• Software and ERP sync
• Raw reads are not inventory. The software must filter duplicates, map EPCs to SKUs or asset records, compare counted quantities with expected quantities, and send adjustments or reports to the ERP, POS or asset register.
MINDWARE

## Slide 6
Phase 4: Baseline, pilot and accuracy measurement
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Take a baseline
• Before RFID, measure the current state in the pilot area: how long a full count takes, how many people it needs, and how accurate the system quantity is. Without a baseline you cannot prove improvement.
• How to measure accuracy properly
• Choose a sample of locations or SKUs in the pilot area (for example 30-50 SKUs or a set of shelves).
• Do a careful physical audit of that sample - counting by hand, slowly, with two people if possible. This is your "truth".
• Compare the system quantity (before RFID) with the truth: this gives baseline inventory accuracy.
• Run the RFID count on the same sample immediately afterwards, with no stock movement in between, and compare it with the truth. This gives the RFID...
MINDWARE

## Slide 7
Phase 4: Baseline, pilot and accuracy measurement (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Investigate every difference: untagged items, damaged tags, tags hidden behind metal, items counted from a neighbouring area, or genuine audit errors.
• Inventory accuracy is often defined as the percentage of SKUs (or locations) whose system quantity exactly matches the physical quantity. State which definition you use and keep it the same before and after.
• Run the pilot
• Tag the pilot area's existing stock, train two or three counters, and run counts at a fixed frequency (for example weekly) for four to eight weeks. Track count time, read accuracy, inventory accuracy, tagging compliance on new receipts and the number of...
• Example: A hospital store pilots RFID on surgical consumables in one store room. The baseline audit shows that system quantities match the shelf for only a portion of SKUs, and the monthly count takes most of a day.
MINDWARE

## Slide 8
Phase 5: Go-live and routine counting
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• After the pilot, roll out area by area. For each area: tag existing stock, switch incoming goods to the tagging rule (source or in-house), train staff, and set a count schedule.
• Daily or several times a week - fast-moving, high-value or high-shrink categories.
• Weekly - the main sales floor and stockroom.
• Monthly or quarterly - slow movers and fixed assets.
• Roles and responsibilities
• Assign clear owners before go-live. A store or stores manager owns the count schedule and signs off adjustments; a small group of trained counters performs counts and searches; the receiving team owns tagging compliance for new goods; and IT or the RFID...
• Write the counting procedure as a one-page standard: route, reader settings, how to handle fitting rooms, carts and returns areas, when to stop stock movement during a count, and how to upload results. New staff should be able to follow it after a short...
MINDWARE

## Slide 9
Phase 5: Go-live and routine counting (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Retire the old full count only when RFID accuracy has been stable for several cycles and auditors or finance agree.
• Illustrative timeline
• Illustrative only, for one store or stockroom with a single product category; larger estates run several areas in parallel.
• Scope and requirements - 1-2 weeks - What is counted, where, how often, which decisions
• Tag testing and selection - 2-3 weeks - Approved tags per product type
• Software setup and ERP mapping - 2-4 weeks (in parallel) - EPC-to-SKU mapping, count app, reports
• Baseline audit - 1 week - Baseline accuracy and count time
MINDWARE

## Slide 10
Equipment checklist
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• RFID labels / hang tags / hard tags - Identify items, cartons or assets - Chosen per material; test on real products
• RFID label printer-encoder - Print and encode labels in-house - Needed unless everything is source tagged
• Desktop encoder - Encode pre-made tags, verify and re-encode - Useful at receiving and for replacements
• Handheld RFID readers - Cycle counts and item search - Plan one per counting team plus a spare
• Fixed readers and antennas at doorways (optional) - Movement between zones, exit monitoring - Add after handheld counts are stable
• Overhead readers (optional) - Continuous zone-level visibility - Higher cost; best for high-value, high-velocity stock
MINDWARE

## Slide 11
Exception handling
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Every RFID count produces exceptions. Decide in advance who handles each type and how:
• Unknown tags - EPCs that are not in the item master. Usually untagged-at-receiving goods, tags from another store or supplier, or encoding mistakes....
• Missing items - expected but not read. Search with the handheld's "find" mode before writing off; check damaged tags, metal shelves, items in carts...
• Extra items - read but not expected in this location. Often misplaced stock or a booking delay; correct the location or transaction.
• Duplicate EPCs - two items with the same code. Re-tag one and fix the encoding process.
• Untagged items - spot-check new receipts for tagging compliance and feed results back to suppliers or the tagging team.
MINDWARE

## Slide 12
KPIs and pitfalls
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• KPIs
• Inventory accuracy % - SKUs or locations where system quantity equals physical quantity.
• Count time - person-hours per count and per area.
• Count frequency - how often each area is actually counted.
• Read accuracy - share of tagged items found by an RFID count versus a controlled audit.
• Shrink - unexplained loss as a share of sales or inventory value, measured the same way before and after.
• Tagging compliance - share of received items correctly tagged and encoded.
MINDWARE

## Slide 13
KPIs and pitfalls (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Out-of-stocks and replenishment accuracy where counts drive replenishment.
• Pitfalls
• Tagging before deciding what decisions the data will support.
• Choosing tags by price alone and discovering poor reads on metal or liquid items.
• No baseline, so improvement cannot be shown.
• Letting new, untagged stock in after go-live, which slowly destroys accuracy.
• Counting with inconsistent routes and technique.
MINDWARE

## Slide 14
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE