## Slide 1
RFID for a Jewellery Store: Step-by-Step Implementation
This is a practical, phase-by-phase plan for rolling out RFID in a jewellery showroom, from the first assessment to daily counts and audits. It assumes you already know why jewellers use RFID and focuses on exactly what to do, in...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/jewellery-store-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Before you start
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• This chapter is a hands-on implementation plan. If you want the overview first - why jewellers use RFID, the types of readers and the benefits - read RFID for Jewellery .
MINDWARE

## Slide 3
The two essentials: RFID jewellery labels + RFID software
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Every jewellery RFID project rests on two things working together: a small RFID label on every piece and jewellery RFID software that knows what each label means. Readers, gates and printers only move data between the two.
• RFID jewellery labels
• Dumbbell / barbell labels - the classic jewellery tag: two printable ends joined by a thin strip that loops through a ring, chain clasp or bangle....
• Rat-tail / tail labels - a single printable flag with a thin tail for threading; good for chains, earrings and small pendants.
• Thread or loop tags - a small hard or flexible RFID tag tied with nylon thread; reusable on display pieces.
• Box and tray labels - larger UHF labels for packed items, trays and pouches so whole trays can be checked at once.
• Each label is printed with what staff need to see - item code, barcode, gross and net weight, purity (karat), stone details, price or price code, and the HUID number - and encoded with a unique EPC that the software links to the item record. Printing and...
MINDWARE

## Slide 4
The two essentials: RFID jewellery labels + RFID software (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Dumbbell / barbell - Rings, bangles, chains, bracelets - Code, barcode, weight, karat, HUID, price - Keep the inlay end away from the metal where...
• Rat-tail / tail - Earrings, pendants, nose pins - Code, barcode, weight - Choose a small inlay tuned for dense trays
• Thread / loop tag - Display and high-value pieces - Code (often on a printed card) - Reusable when items are sold
• Box / tray label - Packed sets, trays, pouches - Tray or box ID, item count - Lets staff check a whole tray at the counter
• RFID jewellery software
• The software turns tag reads into answers. At minimum it should include: an item master (design, karat, weights, stones, making charges, HUID, photo) with the EPC of each label; label printing and encoding ; stock count and reconciliation by counter, tray...
• Where AI adds value
MINDWARE

## Slide 5
Phase 1: Assess your store
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Spend the first week collecting facts. Every later decision depends on them.
• Stock size and mix: how many pieces in total, and how many in each category - gold, diamond, silver, platinum, kundan, loose stones. Small items such...
• Counters and trays: number of counters, trays per counter, typical pieces per tray, and how trays move between counter, display and vault.
• Branches and locations: showrooms, warehouse or vault, karigar workshops, exhibition stock.
• Current software: which billing or ERP system you use, whether it already has item codes, barcodes and HUID fields, and whether the vendor can...
• Current routines: how often you count, how long it takes, and where differences usually appear.
• Write a one-page goal statement, for example "full showroom count in under an hour, every tray checked at opening and closing, karigar stock reconciled weekly". This becomes your measure of success.
MINDWARE

## Slide 6
Phase 2: Choose the tags
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Jewellery tags are small UHF tags in a dumbbell, rat-tail or tail shape, with a print area for the barcode, item code, weight and purity. They are tied to the piece with thread so that the antenna hangs away from the metal.
• Test two or three tag designs on your actual pieces, in your actual trays, before ordering in bulk.
• Check the print area: can you fit item code, gross and net weight, purity, and a barcode at a readable size?
• Check how the tag behaves in a dense tray of chains or bangles, not just on a single item on a table.
• Order spares - typically a margin of 10-15% over your piece count for misprints, re-tagging and new stock.
• Small items need special thought. Nose pins, studs and small pendants are often lighter than the tag itself, so many stores keep such items in tagged pouches, boxes or cards, with one tag per piece on the packaging rather than on the jewel.
• See UHF RFID labels for the general range of tag formats.
MINDWARE

## Slide 7
Phase 3: Clean up the item master
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• RFID makes your stock data visible; it does not fix it. Before tagging, make sure every piece has one clean record with:
• A unique item code (one code per piece, not per design).
• Category, design or style code, and counter or tray location.
• Gross weight, net weight, stone weight and purity or karat.
• The BIS HUID number for hallmarked gold items.
• Stone details for diamond pieces, making charges or price basis as your software requires.
• Physically verify a sample against the records. If the paper count and the system disagree, resolve it now - otherwise the first RFID count will show "missing" items that were never really there.
MINDWARE

## Slide 8
Phase 3: Clean up the item master (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Watch out: Do not let tagging start while master data is half-clean. Every piece tagged against a wrong record has to be found and re-tagged later, which costs far more than the delay.
MINDWARE

## Slide 9
Phase 4: Print, encode and tag existing stock
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Bulk tagging is the most labour-intensive phase. Plan it like a project.
• How to organise it
• Work tray by tray or counter by counter, never randomly. Take one tray off display, tag every piece, read the tray to confirm, and return it.
• Print and encode from the software, so the EPC written to each tag is linked to the item code automatically. See the RFID printers guide and RFID...
• Use a small team: one person prints and checks the data, one ties tags, and a supervisor verifies each finished tray with a reader.
• Set a daily target from a trial day. A trained pair can typically tag a few hundred pieces a day, fewer for complex items needing careful data checks.
• Reconcile every evening: pieces tagged today versus pieces planned, and any tags voided.
MINDWARE

## Slide 10
Phase 4: Print, encode and tag existing stock (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Example: A showroom with about 8,000 pieces and a tagging team of two pairs might plan for roughly three weeks of tagging, done in the morning before peak hours and on the weekly off day, starting with the slowest-moving counters so sales are least disturbed.
MINDWARE

## Slide 11
Phase 5: Place the hardware
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Handheld reader - Shared by floor staff and supervisor - Full store counts, finding a piece, vault counts. See handheld reader guide .
• Counter or tray reader (desktop pad) - Billing counter, tray-issue desk - Reading a tray in seconds, billing by tag read, tray issue and return.
• Encoder or RFID printer - Back office - Tagging new stock and re-tagging.
• Exit gate - Showroom entrance - Alert if an unsold tagged piece passes.
• Vault reader or handheld - Safe / strong room - Night stock check before locking.
• The vault deserves special attention. Steel safes and strong rooms block radio signals, so a reader outside the vault cannot see stock inside it.
• Keep counter readers on low power so they read only the tray on top, not the neighbouring counter. Test the exit gate with staff walking at normal speed carrying a tagged piece in a hand, pocket and bag.
MINDWARE

## Slide 12
Phase 6: Set up software and billing integration
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Load the clean item master and the store layout: counters, trays, vault, karigars, branches.
• Create user roles - salesperson, counter in-charge, manager, auditor - with an audit trail on every edit.
• Link billing: reading a tag at the counter should fetch the item into the bill, and the sale should mark the item sold so it disappears from counts...
• Configure reports: daily count result, missing and extra pieces, tray status, karigar balance, transfer status.
• Set alerts for gate events and for count differences, by SMS, WhatsApp or email.
• For a deeper look at what the software should do, see RFID software: how it works and what to integrate .
MINDWARE

## Slide 13
Phase 7: Pilot on one counter
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Choose one counter with a representative mix - for example a gold chains and rings counter. Run it on RFID for two to three weeks alongside your existing manual count.
• Compare RFID counts with manual counts every day and investigate every difference.
• Note which items read poorly and why: tag position, dense stacking, metal trays, or reader settings.
• Time the opening and closing counts and the billing flow.
• Collect staff feedback and adjust before expanding.
MINDWARE

## Slide 14
Phase 8: Full-store go-live
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Extend counter by counter as tagging completes. Once every counter has passed a week of matching counts, stop the parallel manual count for routine checks (keep periodic manual spot checks as an audit control).
MINDWARE

## Slide 15
Phase 9: Daily routines
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Opening count: trays come out of the vault and are read before going on display; the software compares with last night's closing.
• Tray issue and return: salespeople take a tray against their name and return it; the tray is read at both points.
• Billing: tag read, bill created, tag removed, item marked sold.
• Karigar issue and receipt: pieces sent for repair or alteration are issued against the karigar and checked on return, with weight recorded.
• Closing count: every tray is read before it goes into the vault; differences are resolved before staff leave.
• New stock: tagged on arrival, before display.
• Tip: Make the closing count a fixed sign-off step with a name and time against it. When a difference is found the same evening, it is usually traced in minutes; found a week later, it may never be explained.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE