## Slide 1
RFID for Laundry & Linen: Step-by-Step Implementation
Hotels, hospitals and commercial laundries handle thousands of linen pieces that are hard to count and easy to lose. This chapter is a step-by-step plan for tagging linen with wash-proof UHF tags, counting whole bags and carts...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/laundry-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why RFID for laundry and linen
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Linen moves in a loop: from rooms, wards or restaurants to the laundry, through washing, drying and ironing, and back again - sometimes several times a week. Along the way it is counted by hand, often wet and soiled, by staff under time pressure.
• Lost linen: pieces disappear between the client and the laundry, are taken by guests, or are sent to the wrong client, and nobody can prove where.
• Slow, unhygienic counting: counting soiled hospital linen by hand is unpleasant and carries infection risk.
• Disputes: hotel and laundry each have a different count, and the bill is argued every month.
• Unknown life: no one knows how many times a sheet has been washed, so replacement is guesswork.
• Billing by weight or estimate instead of by actual pieces processed.
• With RFID, every piece carries a unique tag. Whole bags and carts are counted in seconds without handling individual pieces, each piece's history is recorded, and both sides see the same numbers.
MINDWARE

## Slide 3
Why RFID for laundry and linen (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• How the three main users differ
• Hotels care most about guest-room and restaurant linen, bathrobes and premium towels, par levels per floor, and holding their outsourced laundry...
• Hospitals add hygiene: soiled and infected linen should be handled as little as possible, so counting sealed bags without opening them is a major...
• Commercial laundries serve many clients at once. Their priorities are keeping each client's linen separate, proving what was received and returned...
• The steps below work for all three; the emphasis in software and reporting changes with who owns the linen and who pays for losses.
MINDWARE

## Slide 4
Step 1: Choose the laundry tags
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Ordinary paper labels will not survive a wash. Laundry uses purpose-made UHF textile tags, sealed so that water, heat, pressure and chemicals do not damage the chip or antenna.
• What to check
• Wash durability: manufacturers commonly rate laundry tags for around 200 or more industrial wash cycles; this figure is typical, not guaranteed, and...
• Temperature and process: water temperature, tunnel washers, tumble dryers, flatwork ironers and presses. Check the rated maximum temperature and...
• Chemicals: resistance to detergents, alkali, bleach and disinfectants used in hospital processes.
• Size and flexibility: small and soft enough not to be noticed in a hem.
• Attachment options
MINDWARE

## Slide 5
Step 1: Choose the laundry tags (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Sewn-in - Fabric-cased tag stitched into the hem or seam. - Most durable; towels, sheets, uniforms.
• Heat-sealed - Tag with heat-activated adhesive pressed on, sometimes inside a patch. - Faster to apply; check durability on your fabrics.
• Pouch or pocket - Tag placed in a small sewn pocket. - Allows tag replacement; needs care so tags do not fall out.
• Tip: Run a wash trial before ordering in bulk. Tag 50-100 pieces with each candidate tag and method, send them through your real process for several weeks, and check read performance and physical condition regularly.
MINDWARE

## Slide 6
Step 2: Decide tag placement for each linen type
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Pick one position per linen type and keep it consistent. A consistent position protects the tag, makes it easy to find for re-tagging, and improves reading because tags do not all bunch in one place.
• Bed sheet, duvet cover - Corner hem
• Pillow cover - Inside the open-end hem
• Bath and hand towel - Corner of the hem band
• Bathrobe - Inside seam near the neck label or side seam
• Table linen, napkins - Corner hem
• Uniforms, scrubs, gowns - Inside collar or side seam
MINDWARE

## Slide 7
Step 2: Decide tag placement for each linen type (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Avoid areas that go through the flatwork ironer under maximum pressure if your tag is not rated for it, and avoid placing tags where they will be felt against the skin.
MINDWARE

## Slide 8
Step 3: Tag the existing linen
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Load the linen master: linen types, sizes, colours and the owner (hotel, ward or laundry client).
• Encode and register: each tag is read and linked to its linen type and owner in the software, usually at a tagging station with a desktop reader....
• Tag in batches: by linen type and client, as clean linen comes off the line, so pieces are not taken out of circulation.
• Retire old linen first: do not spend tags on pieces that are due for replacement.
• Tag new linen on arrival - many suppliers can supply linen with tags already fitted.
• Watch out: Untagged pieces mixed into tagged stock make every count wrong. Agree a cut-off date after which untagged linen is either tagged at the laundry or rejected.
MINDWARE

## Slide 9
Step 4: Choose how to read
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tunnel or batch reader - A shielded cabinet or tunnel; a whole bag or cart is pushed in and every tag is read in seconds. - Core device for soil-in...
• Handheld reader - Counting linen in store rooms, wards and floor pantries; finding items; checking discrepancies. - See the handheld reader guide .
• Sorting table - A table with an antenna underneath; staff sort pieces by type or client and the screen shows what was read. - Useful where linen from...
• Chute or conveyor reader - Antennas around a chute or conveyor read pieces as they drop or pass. - For high-volume plants with automated handling.
• Door or dock reader - Fixed readers at the laundry dispatch area or hotel linen room. - Records carts leaving or arriving. See fixed reader...
• Wet linen absorbs UHF energy, so soiled counts of very wet loads can be harder than clean counts. Test with realistic loads and bag sizes, and set clear rules for how full a bag may be.
MINDWARE

## Slide 10
Step 5: Set up the laundry software
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Client accounts: each hotel, hospital or department with its own linen pool, prices and par levels.
• Soil and clean counts: counts recorded at collection, at laundry intake and at dispatch, by piece and by type.
• Delivery notes: generated automatically from the clean-out count, with the client acknowledging receipt.
• Discrepancy reports: pieces sent soiled but not returned, pieces returned that were never sent, rejects for stains or damage.
• Wash cycle counting: each pass through the laundry increments the piece's cycle counter.
• Ageing and replacement: flags pieces near end of life and pieces not seen for a set number of days (likely lost).
• Billing: per piece processed, per client, with reports that both sides trust.
MINDWARE

## Slide 11
Step 5: Set up the laundry software (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Integration: with the hotel PMS, hospital systems or accounting software where needed. See RFID software: what to integrate .
MINDWARE

## Slide 12
Step 6: Run the process, step by step
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Collect soiled linen: housekeeping or ward staff bag soiled linen; optionally a handheld or linen-room reader records what leaves.
• Count in: at the laundry, each bag passes through the tunnel reader; the software records the soil-in count against the client.
• Wash and finish: washing, drying, ironing and folding as normal. Tags need no attention.
• Count out: clean linen is packed by client into carts or bundles and read in the tunnel; the count is compared with soil-in.
• Dispatch: the delivery note is generated from the clean-out count and the cart is recorded leaving.
• Client receipt: the client checks the delivery, optionally with its own reader, and confirms. Differences are raised against the specific pieces, not...
• Example: A hospital sends 400 soiled pieces; the laundry's soil-in count shows 396 tags, and the four missing pieces are identified by their tag numbers. When the clean-out count is short by six, the software lists which six pieces are still in process or...
MINDWARE

## Slide 13
Step 7: Pilot
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Start with one linen type (for example bath towels) for one client, floor or ward. Run RFID counts alongside manual counts for a few weeks, investigate every difference, check tag survival after repeated washes, and refine bag sizes, reader settings and staff...
• Agree the pilot success criteria in advance with everyone involved, including the client if you are a commercial laundry: for example, RFID bag counts matching careful manual counts within an agreed tolerance, no measurable damage to tags after a set number...
MINDWARE

## Slide 14
Step 8: Track KPIs
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Linen loss rate per month, before and after.
• Count accuracy: RFID versus spot manual checks.
• Time spent counting per bag or cart.
• Number of billing disputes and time to resolve.
• Average wash cycles at retirement, by linen type.
• Tag failure rate (pieces that stop reading).
• Linen stock against par level per client.
MINDWARE

## Slide 15
Troubleshooting
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Bag count lower than expected - Overfilled or very wet bag; tags shielded in the centre - Limit bag size, allow draining, verify with handheld
• Tunnel reads tags from the next bag - Door left open or poor shielding - Close the tunnel, check shielding and power
• Tags failing early - Process exceeds tag rating, wrong attachment - Review temperature and pressure; change tag or position
• Pieces show as lost but are in use - Linen kept in client stores for long periods - Run handheld counts at client sites; adjust "not seen" threshold
• Wrong client on a piece - Registration error during tagging - Re-register at sorting table; audit tagging station
• When a problem persists, isolate it: read the same bag with a handheld, then the tunnel, then piece by piece on the sorting table. That quickly shows whether the issue is the tag, the load or the reader.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE