## Slide 1
RFID Cost & ROI
What does an RFID system really cost, and how do you know whether it will pay back? This chapter breaks down every cost component with indicative Indian price ranges, works through a complete ROI example in rupees with stated...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/rfid-cost-roi | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
How to think about RFID cost
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• People usually ask "what does an RFID tag cost?" The better question is "what does it cost to solve this problem with RFID, over the life of the system, compared with the value it creates?" Tags are only one part. A credible estimate includes every component...
• Watch out: All prices in this chapter are indicative ranges for the Indian market, exclusive of taxes, for orientation only. Actual prices vary with volume, brand, chip, specification, exchange rates and market conditions.
MINDWARE

## Slide 3
Cost components
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tags
• Tag cost depends on frequency, chip, antenna size, encapsulation, printing, encoding and, above all, volume. Large orders of standard labels are far cheaper per unit than small orders of custom tags.
• UHF paper label or inlay, standard size, in volume - about 4 - 15 - Cartons, retail items, documents
• Printed UHF garment ticket or care label - about 6 - 20 - Apparel source tagging
• HF / NFC label - about 8 - 40 - Libraries, product authentication, smart posters
• Flexible on-metal UHF label - about 30 - 120 - IT assets, metal shelving, cylinders
• Rugged hard tag (on-metal, industrial, high-temperature) - about 60 - 500 or more - Tools, pallets, machinery, outdoor assets
MINDWARE

## Slide 4
Cost components (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Laundry / textile tag - about 50 - 200 - Linen, uniforms
• See our UHF RFID labels and RFID hard tags ranges for options.
• Readers, antennas, printers and accessories
• Desktop / USB reader-writer - about 8,000 - 40,000 - Counters, encoding stations, POS
• Handheld UHF reader - about 60,000 - 3,00,000 - Lower end often a sled paired with a phone; higher end rugged, long range
• Fixed UHF reader (2-8 ports) - about 80,000 - 2,50,000 - Doors, conveyors, workstations
• UHF antenna - about 8,000 - 35,000 each - Plus cables, connectors and mounts
MINDWARE

## Slide 5
One-time vs recurring costs
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Site survey and tag testing - Tags for consumable items (every new item needs a new tag)
• Readers, antennas, printers, handhelds - Software subscriptions or annual licence maintenance
• Reusable tags for assets, crates and pallets - Hardware AMC and spares
• Software licence and configuration - Replacement tags for damaged or lost items
• Integration development - Support staff time, re-testing, cloud or hosting fees
• Installation and initial training - Refresher training for new staff
• Tip: The biggest structural difference between RFID business cases is whether tags are consumed (one per item sold or shipped) or reused (tags on assets, crates and pallets that circulate for years). Reusable-tag projects turn the tag cost into a one-time...
MINDWARE

## Slide 6
The formulas you need
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Keep the maths simple and transparent so anyone can check it:
• Net annual benefit = annual gross benefits - annual recurring costs
• Payback period (years) = initial one-time investment / net annual benefit
• ROI % over N years = (net annual benefit x N - initial investment) / initial investment x 100
• These simple formulas ignore the time value of money. For larger investments, finance teams will also want net present value (NPV) or internal rate of return (IRR), which discount future benefits; the inputs are the same.
MINDWARE

## Slide 7
Worked ROI example: returnable crate tracking in a warehouse
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A food distributor's warehouse ships goods to its distributors in returnable plastic crates. Crates go missing, dispatch is counted by hand, and distributors dispute how many crates and cartons they received.
• Example: Every figure below is an assumption for illustration , not a quote or a benchmark. Replace each one with your own measured data and current quotations.
• Assumptions
• Crate fleet: 20,000 crates; replacement cost Rs 450 per crate.
• Current loss rate: 12 percent per year (2,400 crates). Target with RFID: 4 percent (800 crates).
• Manual counting and reconciliation today: 3 staff at Rs 25,000 per month each; with RFID, 1 is needed and 2 are redeployed to other work.
• Short-shipment claims and disputes avoided: Rs 2,00,000 per year.
MINDWARE

## Slide 8
Worked ROI example: returnable crate tracking in a warehouse (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Crate tag: rugged UHF tag at Rs 40 each, buying 22,000 including 10 percent spares.
• One-time investment (indicative)
• Crate tags - 22,000 x 40 - 8,80,000
• Tag application labour - 20,000 x 3 - 60,000
• Dock-door portals - 2 x (reader 1,80,000 + 4 antennas 60,000 + cabling, mounts, lights 60,000) - 6,00,000
• Handheld readers - 2 x 1,50,000 - 3,00,000
• Software and ERP integration - Estimate - 6,00,000
MINDWARE

## Slide 9
A note on item-level tagging economics
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• When every item carries a consumable tag, compare the tag cost with the item's margin, not just its price. For example, a Rs 8 tag on a garment selling at Rs 1,200 with a 40 percent gross margin (Rs 480) consumes about 1.7 percent of that item's margin.
MINDWARE

## Slide 10
Hidden costs to include
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tag testing and samples - several tag types and placements, sometimes repeated.
• Master data cleaning - fixing duplicate or wrong item and asset records before tagging.
• Initial tagging effort - tagging existing stock or assets, often in a short window.
• Process change and parallel running - staff time while old and new processes overlap.
• Civil and electrical work - power points, network cabling, mounting structures, enclosures.
• Infrastructure changes - Wi-Fi coverage for handhelds, servers or cloud hosting.
• Exceptions handling - staff time to resolve missed or unexpected reads.
MINDWARE

## Slide 11
Hidden costs to include (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Hardware refresh - readers and handhelds have finite life; plan for replacement over a five-year horizon.
• Internal project time - managers and IT staff spend time on the project even if no invoice is raised.
MINDWARE

## Slide 12
How to build a business case
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• State the problem in numbers : losses, labour hours, errors, lost sales, penalties.
• Measure the baseline for each KPI over a representative period.
• List every cost using the components above, split into one-time and recurring, with quotes where possible.
• Estimate benefits conservatively , and show which are hard savings (cash) and which are soft (time, service).
• Calculate payback and ROI with the simple formulas, and NPV if finance requires it.
• Run a sensitivity check on the two or three assumptions that matter most.
• Propose a pilot with success criteria that will validate those assumptions before full investment.
MINDWARE

## Slide 13
How to build a business case (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The implementation guide explains how to structure that pilot, and the chapter on advantages and disadvantages helps you present risks honestly.
MINDWARE

## Slide 14
Ways to reduce RFID cost
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Pilot first. Spending a small amount to learn which tag, antenna layout and process works avoids buying the wrong thing in bulk.
• Choose the right tag, not the most expensive one. Select the lowest-cost tag that meets your tested performance target. A premium industrial tag on a...
• Roll out in phases. Start with the process or site with the clearest payback and let early savings fund the next phase.
• Reuse tags where possible on crates, pallets, totes, assets and textiles.
• Tag at the right level. Case or pallet tagging may deliver most of the value at a fraction of item-level cost.
• Use handhelds before fixed infrastructure where periodic counts are enough.
• Buy labels at sensible volumes with standard sizes, and consider supplier source tagging.
MINDWARE

## Slide 15
Ways to reduce RFID cost (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Standardise on one tag specification and one reader configuration across sites.
• If you would like help estimating costs and benefits for your own operation, our RFID consulting team can prepare an independent business case.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE