## Slide 1
RFID Read Range & Performance
Read range is the first question everyone asks about RFID, and the answer is always "it depends". This chapter explains exactly what it depends on, gives typical ranges by frequency band, explains forward and reverse links, and...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/rfid-read-range | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why read range "depends"
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Ask any RFID engineer "How far does it read?" and the honest answer is "It depends." That is not evasion. Read range is the result of a chain of factors, and the weakest link sets the limit.
• This chapter explains each link in that chain so you can predict, measure and improve range. It builds on RFID Antennas & Inlays and RFID Readers Explained .
MINDWARE

## Slide 3
What determines read range
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• On the reader side
• Reader output power: the RF power fed to the antenna, typically up to about 30 dBm (1 W) for fixed UHF readers, limited by regulation.
• Cable and connector loss: every dB lost in cables reduces the power reaching the antenna and weakens the tag's reply on the way back.
• Antenna gain and beamwidth: higher gain focuses energy for more range along the beam but covers less width.
• Polarisation: circular antennas read tags in any rotation but give up about 3 dB against a perfectly aligned linear antenna.
• Receiver sensitivity: how weak a tag reply the reader can still decode.
• On the tag side
MINDWARE

## Slide 4
What determines read range (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Chip sensitivity: how little power the chip needs to wake up - see RFID Chips Explained .
• Antenna size and design: larger, well-matched antennas capture more energy.
• Tuning for region and material: a tag tuned for 915 MHz or for plastic may lose range at 866 MHz or on cardboard.
• Orientation: a linear dipole tag reads worst when it points end-on toward the antenna, and poorly when rotated 90 degrees to a linear antenna.
• In the environment
• Metal: reflects UHF energy, detunes tags and creates shadows and dead spots - but can also bounce signals into unexpected places.
• Liquids and water-rich products: absorb UHF energy; tags on or behind liquids read poorly.
MINDWARE

## Slide 5
Typical read ranges by band
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• The figures below are indicative for common passive tags in reasonable conditions. They are not guarantees - test on your own items.
• LF 125-134.2 kHz (passive) - A few cm to around 10-30 cm; larger with big antennas - Robust near water and tissue; slow data rate
• HF 13.56 MHz, ISO 14443 / NFC - Up to about 10 cm (phones: typically up to about 4 cm) - Short range by design; payments, access, NFC
• HF 13.56 MHz, ISO 15693 - Up to about 1 m with large reader antennas - Libraries, healthcare, industrial labels
• UHF passive, handheld reader - Typically 1-6 m for labels - Depends on handheld power and antenna
• UHF passive, fixed reader - Typically 3-10 m for good labels; beyond 10 m for large tags - Strongly affected by materials and orientation
• UHF on-metal hard tags - From under 1 m for tiny tags to several metres for large ones - Range scales with tag size
MINDWARE

## Slide 6
Typical read ranges by band (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• For a deeper comparison of the bands, see RFID Frequencies .
MINDWARE

## Slide 7
Forward link and reverse link
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A passive UHF read is a round trip, and both directions must succeed:
• Forward link (reader to tag): enough power must reach the tag to exceed the chip's read sensitivity, so the chip can wake up and respond.
• Reverse link (tag to reader): the tag's backscattered reply - a tiny fraction of the power it received - must travel back and arrive above the...
• With modern readers, the receiver is usually so sensitive that it could hear a tag further away than the tag can be powered. So passive UHF is normally forward-link limited : the tag runs out of power before the reader stops hearing it.
• There are exceptions. In noisy environments with many readers, with very small tags, or with battery-assisted tags (which do not need the reader's energy to power the chip), the reverse link can become the limit.
• The 6 dB rule
• In free space, received power falls with the square of distance. A useful rule follows: every 6 dB of extra link budget roughly doubles range, and every 6 dB lost halves it .
MINDWARE

## Slide 8
Forward link and reverse link (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Example: A dock door reads tags at 4 m. The installer replaces 8 m of thin cable (about 3 dB loss) with a short low-loss cable (under 0.5 dB).
• Real environments with reflections rarely follow free-space maths exactly, but the rule is good for comparing options.
MINDWARE

## Slide 9
Read rate vs read accuracy
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Two different performance measures are often confused:
• Read rate is speed: how many tag reads per second the reader can perform. Datasheets quote peak values in ideal conditions.
• Read accuracy is correctness: the percentage of tags that should be read that actually are, without reading tags that should not be. A portal that...
• Most business cases depend on accuracy, not raw speed or maximum range. A 100% accurate read zone of 2 m is far more useful than an unpredictable 8 m zone.
MINDWARE

## Slide 10
Interference, multipath and stray reads
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Multipath and nulls
• UHF signals reflect off metal racks, floors, walls and vehicles. Reflected waves combine with the direct wave, adding in some places and cancelling in others.
• Stray reads
• The other side of reflections is stray reads : tags read where you did not intend - in the next dock door, on a shelf behind the portal, or in a staging area. Stray reads damage accuracy just as much as missed reads.
• Reader-to-reader interference
• Multiple readers close together can interfere. Use dense reader mode settings, coordinate channel and timing where the reader supports it, and avoid running every reader at full power continuously.
• Watch out: Turning reader power to maximum is the most common "fix" and often the worst one. It may add range but almost always adds stray reads and interference.
MINDWARE

## Slide 11
Practical tuning tips
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Get the tag right first. Test several tags on the actual item; the right tag solves more problems than any reader setting.
• Find the best spot on the item. Move tags away from metal edges and liquid contents; on cartons, place tags where they will not be sandwiched between...
• Match polarisation to orientation. Circular for random orientation; linear where tags are consistently aligned.
• Minimise cable loss. Short, low-loss cables; fewer adapters.
• Use power and RSSI filtering. Lower power to tighten zones; in software, use signal strength, antenna port and timing to reject stray reads.
• Trigger with sensors. Photo-eyes and motion sensors limit reading to the moments that matter.
• Test at real speed and density. Forklift speeds and full pallets behave differently from hand-held tests.
MINDWARE

## Slide 12
Practical tuning tips (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Document settings. Record power, sessions, antenna positions and results so the configuration can be reproduced and maintained.
• Tip: A structured test plan - fixed distances, orientations, materials and pass criteria - turns tuning from guesswork into engineering. Our Site Survey & Tag Testing chapter provides a template.
MINDWARE

## Slide 13
Troubleshooting table
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Tags read on the desk but not on the product - Detuning by metal or liquid in the product - Use on-metal or liquid-tolerant tags; reposition tag; add...
• Some tags on a pallet are always missed - Tags shadowed by product, buried in the middle, or facing end-on - Add antennas from more angles...
• Range much shorter than expected everywhere - Wrong region setting or region-mismatched tags, high cable loss, low power setting - Set reader to...
• Tags read in the next dock door or room - Too much power, antennas aimed at neighbouring areas, reflections - Lower power; re-aim antennas; use...
• Tag reads in one spot, fails a few centimetres away - Multipath null - Use frequency hopping, multiple antennas, or move items through the zone
• Tags not read when carried by people - Body absorbing UHF energy - Antennas on both sides and overhead; tags positioned away from the body; slower...
• If you have tried these steps and still struggle, an on-site RF assessment usually finds the cause quickly. Our RFID consulting team performs site surveys and tag tests, and our Certified RFID Specialist Program teaches hands-on tuning in depth.
MINDWARE

## Slide 14
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE