## Slide 1
RFID Security & Privacy
RFID is neither as dangerous as the myths suggest nor automatically secure. This chapter explains the real threats - cloning, skimming, relay, tampering, jamming and data leakage - the defences available at UHF, HF and NFC, and...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/rfid-security-privacy | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Think in threats, not headlines
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• RFID security discussions tend to swing between two extremes: "RFID can track you anywhere" and "it is just a label, there is nothing to secure". Both are wrong.
• A garment label in a retail store, a FASTag on a car windscreen, an employee access card and a drug authentication tag face very different threats. A stock-count label mainly needs integrity of data; an access card needs resistance to cloning; a hospital...
• What happens if someone copies a tag?
• What happens if someone reads a tag without permission?
• What happens if tags or readers stop working?
MINDWARE

## Slide 3
The main RFID threats
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Cloning - Reading a tag's identifier (and any readable data) and writing it to another tag or emulator - Access cards, anti-counterfeit labels...
• Skimming - Reading a tag without the owner's knowledge using a hidden or unauthorised reader - ID cards, payment cards, tagged items carried by people
• Eavesdropping - Listening to a legitimate reader-tag conversation from a distance - Systems that send sensitive data or passwords unencrypted
• Relay attack - Two attacker devices forward signals between a genuine card and a distant reader in real time - Contactless access and payment...
• Tag tampering - Rewriting unlocked memory, swapping tags between items, or physically damaging tags - Retail, asset tracking, supply chains with...
• Denial of service / jamming - Radio interference, shielding goods in foil, mass-killing tags with a known kill password - Security gates, EAS...
• Note that the backend is part of the attack surface. Many real incidents involve insecure servers, default reader passwords or exposed APIs rather than clever radio attacks.
MINDWARE

## Slide 4
Myths vs reality
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Passive RFID tags can be read from kilometres away. - Passive UHF tags are powered by the reader's signal, which limits practical range to metres ...
• An RFID tag can track my location like GPS. - Passive tags have no battery, GPS or radio of their own. They can only be detected where a reader is...
• Every RFID tag stores my personal details. - Most tags store only an identifier. The personal link, if any, exists in a database - which is where...
• A contactless payment card can be emptied by brushing past it. - Payment cards generate one-time cryptograms and are subject to transaction limits...
• RFID is inherently secure because it is radio. - Basic tags offer little security. Security comes from choosing cryptographic chips and designing the...
• Tip: Eavesdropping range is different from read range. The reader's own transmission is strong and can sometimes be received from much farther away than a tag's weak reply.
MINDWARE

## Slide 5
Defences for UHF (EPC Gen2) tags
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Lock, passwords and kill
• Standard Gen2 tags provide a 32-bit access password, a 32-bit kill password and lock states for each memory bank (see EPC Encoding & Tag Memory ). Use them:
• Lock the EPC and User memory with a non-default access password so tags cannot be rewritten by anyone with a reader.
• Read-lock both passwords so they cannot be retrieved.
• Prefer unique per-tag passwords, for example derived from the TID and a secret key held in your system, so one leaked password does not unlock...
• Use the kill command at point of sale where customer privacy matters and the tag has no after-sale use.
• These controls stop casual tampering, but the Gen2 password mechanism was not designed as strong cryptography and should not be relied on against a determined attacker.
MINDWARE

## Slide 6
Defences for UHF (EPC Gen2) tags (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• TID checks
• Recording the factory TID next to each EPC and checking both on read detects simple clones made with ordinary blank tags. It is a cheap and effective first layer, though specialist emulators can fake a TID.
• Gen2v2 features
• Gen2v2 adds optional commands that substantially improve security and privacy on chips that implement them:
• Untraceable - a tag can hide all or part of its EPC, TID and User memory, and reduce its operating range, so only authorised readers see full data....
• Authenticate - cryptographic challenge-response using crypto suites from the ISO/IEC 29167 family (for example AES-128 based), proving that a tag is...
• Chip support varies, and readers and software must support these commands too, so verify end to end before committing. Chip families are compared in RFID Chips Explained .
MINDWARE

## Slide 7
Defences for HF and NFC tags
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Avoid broken legacy chips for security
• The proprietary Crypto-1 cipher in MIFARE Classic cards was publicly broken in 2008, and those cards can be cloned with readily available tools. Plain 125 kHz proximity cards are even weaker: most simply broadcast a fixed number.
• MIFARE DESFire (EV1, EV2, EV3)
• DESFire chips are ISO/IEC 14443 A cards with on-chip AES-128 encryption, mutual authentication between card and reader, and file-based access rights per application. Keys never leave the chip.
• NTAG 424 DNA and SUN messages
• NTAG 424 DNA is an NFC Forum Type 4 tag with AES-128. Its standout feature is Secure Dynamic Messaging (SDM) , which produces SUN (Secure Unique NFC) messages: every time a phone taps the tag, it returns a URL containing an encrypted tag ID, a tap counter and...
• Example: A premium tea exporter puts an NTAG 424 DNA tag under the seal of each tin. When a buyer in Dubai taps the tin with a phone, the browser opens the brand's verification page, which checks the SUN signature and counter and shows "Genuine product, first...
MINDWARE

## Slide 8
Defences for HF and NFC tags (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• See our NFC tags and RFID cards and wristbands pages for secure options.
MINDWARE

## Slide 9
Physical and backend defences
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Shielding
• Metal foil and conductive fabrics block RF energy. RFID-blocking sleeves and wallets protect cards when fully enclosed; shielded pouches protect passports and ID documents.
• Backend authorisation
• The strongest principle in RFID security is: a tag ID is a claim, not a proof . Decide what a tag read is allowed to do in the backend, using business context:
• Check that the tag is active, not reported lost, and associated with the expected item or person.
• Check plausibility - the same card cannot enter Gate 1 in Delhi and Gate 4 in Pune within a minute.
• For sensitive actions, add a second factor such as a PIN, biometric or camera check.
MINDWARE

## Slide 10
Physical and backend defences (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Secure readers, networks and APIs as described in RFID Middleware & Software .
• Relay and jamming
• Relay attacks are hard to stop with crypto alone because the genuine card performs the cryptography. Defences include proximity-check features, tight timing limits, requiring user action and transaction limits.
MINDWARE

## Slide 11
Privacy by design
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Privacy concerns arise when an RFID tag becomes linked to a person - an employee badge, a student card, a patient wristband, a tagged garment after purchase. Build privacy in from the start:
• Data minimisation - store only a random or opaque reference on the tag, never names, Aadhaar numbers, phone numbers or health details.
• Purpose limitation - use location data collected for safety or attendance only for that purpose, not for unrelated monitoring.
• Transparency - tell people where readers are and why; visible signs at reader zones build trust.
• Control at end of use - kill, detach or deactivate consumer tags at sale, or use Gen2v2 Untraceable.
• Retention limits - delete or anonymise movement histories when they are no longer needed.
• Access control and audit - restrict who can see personal location data and log every access.
MINDWARE

## Slide 12
Privacy law: India's DPDP Act and global rules
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• This section is a high-level overview, not legal advice.
• India - Digital Personal Data Protection Act, 2023
• The DPDP Act governs digital personal data processed in India, and processing outside India connected with offering goods or services to people in India. RFID data becomes personal data when it can identify a person, directly or by linking a tag ID to an...
• Processing for a lawful purpose, on the basis of consent or a legitimate use recognised by the Act, with a clear notice.
• Collecting only what is needed for that purpose and keeping it accurate.
• Implementing reasonable security safeguards to prevent personal data breaches.
• Notifying the Data Protection Board and affected individuals of breaches.
MINDWARE

## Slide 13
Privacy law: India's DPDP Act and global rules (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Honouring the rights of individuals ( Data Principals ), such as access, correction, erasure and grievance redressal.
• Extra care for children's data, including verifiable parental consent - relevant for school RFID attendance systems.
• Penalties under the Act can be very large, so RFID projects involving people should include a privacy review from the start. Detailed rules made under the Act are being implemented in phases, so check the current position with your legal team.
• Elsewhere
• In the European Union, the GDPR treats RFID data linked to a person as personal data, and European guidance encourages privacy impact assessments for RFID applications and standard signs that inform people of RFID reading zones. Other countries, including...
• Watch out: Anonymous tags do not stay anonymous once linked. A loyalty card scanned at checkout can connect a customer to every tagged item in the basket.
MINDWARE

## Slide 14
RFID security and privacy checklist
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Threat model written: what happens if a tag is cloned, skimmed or jammed?
• Chip chosen for the risk: plain IDs for logistics; AES-capable chips (DESFire, NTAG 424 DNA, Gen2v2 Authenticate) for access, authentication and...
• No MIFARE Classic or plain 125 kHz cards protecting high-value assets or sensitive areas.
• EPC and user memory locked with non-default, preferably per-tag, access passwords; passwords read-locked.
• TID recorded at encoding and checked in sensitive processes.
• No personal data on tags; opaque references only.
• Backend authorisation, plausibility checks and second factors for sensitive actions.
MINDWARE

## Slide 15
RFID security and privacy checklist (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Readers hardened: default passwords changed, firmware current, separate network segment, TLS for integrations.
• Monitoring for reader outages, unusual silence and RF noise.
• Privacy notice, signage, retention policy and DPDP review completed where people are involved.
• Key management plan: who holds AES keys, how they are stored, rotated and backed up.
• For a review of an existing system or help choosing secure tags, talk to our RFID consulting team. Security design is also covered in depth in our Certified RFID Specialist Program .
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE