## Slide 1
RFID for Warehouse Management: Step-by-Step Implementation
RFID in a warehouse verifies goods automatically as they are received, stored, picked and dispatched, and tracks returnable crates and pallets that usually go missing. This chapter explains how to map processes, choose the...
Indian RFID - Mindware, New Delhi | From consultation to implementation
www.indianrfid.com/rfid-academy/warehouse-rfid-step-by-step | +91-9717122688 | gm@indianbarcode.com
MINDWARE

## Slide 2
Why RFID in the warehouse
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A warehouse runs on confirmations: this pallet arrived, it went to that location, these cartons were picked for this order, this load left on that truck. With barcodes, each confirmation needs someone to find a label and scan it, and when people are busy...
• RFID is not magic, though. It works best when the process is clear, the tag level is right, read points are engineered, and the warehouse management system (WMS) knows what to do with the events.
MINDWARE

## Slide 3
Phase 1: Map processes and choose the tag level
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Process mapping
• Walk the warehouse with the operations team and draw every step from gate-in to gate-out: unloading, receiving, quality check, put-away, replenishment, picking, packing, staging, loading and returns. For each step record what is confirmed today, how, how long...
• For each candidate step, capture a baseline: average time per truck or order, error rates reported by customers or audits, labour hours, and losses such as unreturned crates. Note physical constraints too - door widths, dock levellers, metal racking, product...
• Tag level: pallet, case or item
• Pallet / load unit - SSCC - Full-pallet receiving, put-away, dispatch - Cheapest; no visibility of contents unless linked to ASN
• Case / carton - SGTIN (or SSCC for logistic units) - Case picking, mixed pallets, shipment verification - More tags; dense pallets need read testing
• Item - SGTIN - High-value goods, apparel, each-picking, returns - Highest tag cost; best if source tagged
MINDWARE

## Slide 4
Phase 1: Map processes and choose the tag level (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Returnable asset - GRAI or a company scheme - Crates, pallets, roll cages, totes - Rugged reusable tags; tracked across sites
• EPC Gen2 tags can carry GS1 identifiers so that RFID and barcode data refer to the same unit; how SSCC, SGTIN and other schemes are written into tag memory is explained in EPC encoding and memory . Agree the encoding scheme with suppliers and customers early...
MINDWARE

## Slide 5
Phase 2: Receiving and put-away
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Receiving with dock door portals
• At inbound doors, antennas on both sides of the door frame (and sometimes above) form a portal. As a forklift or pallet jack brings goods through, the reader captures pallet and case tags.
• Put-away
• Put-away can be confirmed in two common ways. In the first, location tags are fixed to racks or floor positions and a reader on the forklift or a handheld reads both the pallet tag and the location tag when the pallet is placed.
• Forklift-mounted readers
• A forklift-mounted system typically combines a rugged vehicle-mounted reader, one or more antennas aimed at the forks (and sometimes upward or downward at location tags), and a vehicle-mounted terminal running the WMS client. Sensors on the forks or mast tell...
• Tip: Stick pallet tags at the same height and on two adjacent faces (for example front and one side). Consistent placement makes dock door and forklift reads far more reliable than any amount of reader tuning.
MINDWARE

## Slide 6
Phase 3: Storage, picking and dispatch
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Storage and cycle counts
• Handheld readers make cycle counts of racked stock much faster, especially for case-tagged goods on accessible levels. High bays may need readers on extended poles or on a forklift.
• Picking and packing verification
• At packing stations, a reader under or around the table reads all tagged items or cases in the order at once and compares them with the order lines. Wrong items, missing items and over-picks are flagged before the carton is sealed.
• Dispatch and load verification
• At outbound doors, the portal reads pallets and cases as they are loaded and checks them against the shipment or load plan for that truck. If a pallet for another customer passes through the wrong door, the system alarms immediately.
MINDWARE

## Slide 7
Dock door design with direction detection
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• A dock door is the hardest read point in most warehouses, because goods are staged nearby, forklifts move in both directions and adjacent doors are close together. A robust design includes:
• Two read zones - antennas facing the dock side and antennas facing the warehouse side, on separate reader ports.
• Presence sensors - photo-eyes or motion sensors that start and stop reading only when something passes, so staged goods are not counted.
• Direction logic - comparing first-seen zone, timestamp order and signal-strength trends to decide in or out.
• Read-zone control - tuned power, antenna angle and, where necessary, RF-absorbing panels to prevent reads from neighbouring doors.
• Operator feedback - a stack light, screen or buzzer showing success or exceptions.
• Cabling, accessories and the details of in/out logic are covered in fixed reader installation . In India, configure readers for 865-867 MHz and keep radiated power within 4 W EIRP (about 1 W transmitter output).
MINDWARE

## Slide 8
Dock door design with direction detection (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Watch out: Never allow staging lanes directly inside the read zone of a dock door. Pallets waiting for a truck will be read again and again, and if direction logic is weak they may be posted as dispatched before they have left.
MINDWARE

## Slide 9
Returnable assets, yard and gate
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Crates, pallets and roll cages
• Plastic crates, pooled pallets, roll cages and totes travel between warehouses, stores, suppliers and customers, and a share of them never comes back. Tagging each asset with a rugged, permanently fixed tag and reading it at dock doors lets you see how many...
• Yard and gate
• Vehicles entering and leaving the warehouse yard can be identified with UHF windshield tags at the gate, linked to appointment and dock scheduling systems. The design is similar to a vehicle access lane - see RFID for car parking for readers, barriers...
MINDWARE

## Slide 10
WMS integration
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• RFID reads only become useful when they turn into WMS transactions. A typical architecture has readers sending raw reads to middleware or an edge controller, which filters duplicates, applies direction logic, groups reads into events (for example "pallet X...
MINDWARE

## Slide 11
Step-by-step: pilot and rollout
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Map processes and choose one flow and one dock door for the pilot.
• Decide tag level and encoding - pallet, case or item; SSCC, SGTIN or GRAI.
• Test tags on real pallets and cartons, including metal and liquid products and dense mixed pallets.
• Design and install the pilot dock door with two zones, sensors and feedback.
• Integrate with the WMS for that flow - ASN check, load verification or crate tracking.
• Run the pilot for four to eight weeks, comparing RFID results with manual checks.
• Fix issues - tag placement, pallet build rules, door tuning, exception workflows.
MINDWARE

## Slide 12
Step-by-step: pilot and rollout (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Roll out door by door and process by process, training each shift.
• Operate and improve - weekly exception reviews, spare readers and antennas on site, and periodic read-rate tests.
• Illustrative timeline
• Illustrative only, for a mid-sized warehouse piloting one dock door; multi-site projects take longer.
• Process mapping and business case - 2-3 weeks - Target flows, baseline KPIs
• Tag level, encoding and tag testing - 2-4 weeks - Approved tags, placement rules
• Pilot dock door design and installation - 2-3 weeks - Working portal with direction detection
MINDWARE

## Slide 13
Equipment checklist
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Fixed readers and antennas (portal sets) - Inbound and outbound doors - Receiving and dispatch verification
• Photo-eyes / motion sensors, stack lights - Each portal - Triggering, direction, operator feedback
• RF-absorbing panels (if needed) - Between adjacent doors - Prevent cross-reads
• Vehicle-mounted readers, antennas, terminals - Forklifts - Put-away and picking confirmation
• Location tags - Racks / floor positions - Precise put-away confirmation
• Handheld readers - Storage areas - Cycle counts, search, exceptions
• Example: A distributor delivering to retail stores in reusable plastic crates tags every crate and installs portals at two outbound and one returns door. Within the pilot period, the reports show which routes return fewer crates than they take, and the...
MINDWARE

## Slide 14
KPIs and pitfalls
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• KPIs
• Receiving time per truck or per pallet, from dock arrival to stock available.
• ASN match rate and time to resolve receiving exceptions.
• Dispatch errors - wrong, short or extra shipments reported by customers.
• Inventory accuracy - WMS quantity vs physical, by location.
• Crate / pallet loss - assets not returned per period, by route or customer.
• Portal read rate - share of tagged units read on a single pass.
MINDWARE

## Slide 15
KPIs and pitfalls (cont.)
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
• Pitfalls
• Installing portals before fixing pallet build and tag placement rules.
• Staging goods inside read zones.
• Treating RFID as a hardware project and leaving WMS integration until last.
• Expecting 100% reads of every carton in dense mixed pallets without testing.
• Not planning how suppliers will tag at source, so in-house tagging becomes a bottleneck.
• Getting the design right first saves money later. Indian RFID's warehouse RFID consulting starts at USD 4,000 for a 2,000-5,000 sq ft facility.
MINDWARE

## Slide 16
Indian RFID - Mindware: from consultation to implementation
Indian RFID - Mindware | www.indianrfid.com | +91-9717122688 | gm@indianbarcode.com
1 Consultation
2 Site survey
3 Pilot
4 Supply
5 Encoding & software
6 Installation & training
7 Support & AMC
Mindware (New Delhi, since 1997) and its RFID division Indian RFID take your project from the first conversation to a working system - and support it after go-live.
Phone / WhatsApp: +91-9717122688 Email: gm@indianbarcode.com
S-4, Pankaj Plaza, Pocket-7, Plot-7, Dwarka Sector-12, New Delhi - 110078
www.indianrfid.com | Free guides: www.indianrfid.com/whitepapers
MINDWARE